## Slide 1: Thermal radiation
Basics
Thermal radiation of
  Gases
  Liquids, Solids
Previous papers
  Species detection
  Surface temperature measurements
IR cameras

## Slide 2: Thermal radiation
Wave / photons
  Wave: liquids, solids, interfaces
  Photon: gases
Energy, speed of light, frequency, wavelength:
  c=c0/n, c0=2.998e8 m/s
  c=λν
  E=hν=hc/λ, h=6.626e-34 J.s: λ↗=>E↘

## Slide 3: Thermal radiation
Blackbody emissive power:
  Ebb(T,ν)=2πhν3n2/[c02.(ehν/kT-1)] W/(m2.s)
  Ebb(T,λ)=2πhc02 /[n2λ5.(ehc/λkT-1)] W/(m2.μm)

## Slide 4: Thermal radiation
Non-Blackbody emissive power:
  E(T,λ)=ελ.Ebb(T,λ)
  E(T) =
Kirchoff’s law
  αλ= ελ: at each wavelength, the emissivity is equal to the absorptivity.
ελ depends on pressure and temperature
Integrated energy on solid angle Ω
  Etot (T) =

## Slide 5: Thermal radiation
α+ρ+τ=1
Radiation of gases
  Internal energy: electronic, vibrational, rotational
  Quantification: only discrete values of photon energy hν can be absorbed/emitted
  In case of thermal radiation, only vibrational and rotational levels are concerned.

## Slide 6: Thermal radiation
Radiation of gases
  Stretching vs bending
  N2, O2,…: no dipole moment, no radiation.

## Slide 7: Thermal radiation
Radiation of gases
  Group frequencies

## Slide 8: Thermal radiation
http://irina.eas.gatech.edu/EAS8803_Fall2009/Lec6.pdf

## Slide 9: Thermal radiation
Radiation of solid and liquids
  Only caused by interaction of photons with free electrons
  Free electrons can absorb or emit photons, modifying their kinetic energy. Since kinetic energy is not quantified, no spectral bands.
  In solids, also lattice vibration (phonon, crystal vibration)

## Slide 10: Previous work
Species detection – 1D measures
  SAE 2007-01-0644: Grosch (Laser-Lab Gottingen). Fuel absorption @3.39μm (using a He-Ne laser) . SI engine. Fuel concentration near spark plug. Sapphire fiber, no absorption @ 3.39 μm.
  SAE 2007-01-0639: Kakuho (Nissan), Hanson (Stanford). 2 colors Water absorption in near IR (around 1.4μm) + modulation. SI engine. Residual gas concentration and temperature near spark plug.
  SAE 2007-01-1849: Kawahara (Obayama Univ.) CO2 absorption at 4.26μm . SI engine. Residual gas concentration.
  SAE 2006-01-3337: De Francqueville (IFPEN). CO2 absorption at 4.26μm. SI engine. Residual gas concentration.
Species detection – 2D measures
  SAE 1999-01-3494: Jansons (Rutgers). IR camera 2000Hz DI Diesel engine. Simultaneous IR emissions @ 2.2μm, 2.47μm (water), 3.42μm (preflame) and 3.8μm (soot). Qualitative images.
  SAE 2000-01-1800: Jansons (Rutgers). IR camera 2000Hz SI and DI Diesel engines. Simultaneous IR emissions @ 2.2μm, 2.47μm (water), 3.42μm (preflame) and 3.8μm (soot). Qualitative images.
  IJER 2008 9:215: Jansons (Wayne State), Lin & Rhee (Rutgers). IR camera 1880Hz SI and DI Diesel engines. Simultaneous IR emissions @ 2.1μm, 2.47μm (water), 3.43μm (preflame) and 3.8μm (soot). HITRANS modelling. HCHO signal week for SI engines.
  SAE 2011-01-1395: Squibb (Michigan State). FLIR Phoenix MID, 60Hz. 3-5μm. 20μs integration time. Fuel sprays and combustion visualization. In-cylinder temperature.
Composite cycle
Composite cycle

## Slide 11: Previous work
Surface temperature
  App. Catal. A (2009) 365:301-308: Shakir (Waterloo Univ)
  SAE 2010-01-1214: Epling (Waterloo Univ)
  2D surface temperature of a catalyst. FLIR Merlin camera 1-5.4μm
  SAE 2014-01-1446: Schulz (Magdeburg Univ.). 2D temperature measurements of a heated plate (80degC) impacted by gasoline sprays. 800Hz, 2 – 5.7μm.

## Slide 12: IR cameras. FLIR vs TELOPS
Chart: Total number of pixels
| 327680 | 204800 | 179200 | 163840 | 81920 | 40960 | 28160 | 20480 | 10240 | 5120 | 2560
FLIR SC6800 | 565 | 980 | 1011 | 1101 | 2093 | 3808 | 5118 | 6450 | 9873 | 13440 | 16404
Telops FAST IR 1500 | 1500 | 7500 | 25000 | 75000
64x8
320x256
64x64
128x128
640x512
640x128
640x32
Max frame rate
1degV @ 1250rpm
No square windowing for FLIR

## Slide 13: IR cameras. FLIR vs TELOPS
Integration time
Max Photons = Max Energy = Φ3-5μm(T).τ
Data FLIR: F/2.5
Temp range (degC) | Pbb: Corresponding BB emissive power (Planck's law) integrated between 3mu et 5mu | Tint: Recommended integration time | Ebb=Pbb*Tint: Energy emitted by the BB during the integration time | Maximum frame rate based on integration time
degC | W/m2/mu | ms | J/m2/mu | Hz
-20 to 50 | 0.78 to 15 | 1.1424 | 0.89 to 17.14 | 875
10 to 90 | 3 to 39 | 0.472 | 1.42 to 18.41 | 2119
35 to 150 | 7.7 to 148 | 0.1321 | 1.02 to 19.55 | 7570
80 to 200 | 30.3 to 350 | 0.0568 | 1.72 to 19.88 | 17606
150 to 350 | 148 to 2130 | 0.0094 | 1.39 to 20.02 | 106383
Data Telops: F/2.3 + fill factor 80pc
Integration time for Telops FAST IR 1500 |  |  |  | 
Temp range (degC) | Pbb: Corresponding BB emissive power (Planck's law) integrated between 3mu et 5mu | Tint: Recommended integration time | Ebb=Pbb*Tint: Energy emitted by the BB during the integration time | Maximum frame rate based on integration time
degC | W/m2/mu | ms | J/m2/mu | Hz
0 | 1.988 | 0.48 | 0.95424 | 2083
50 | 12.6 | 0.19 | 2.394 | 5263
100 | 50 | 0.06 | 3 | 16667
150 | 148 | 0.022 | 3.256 | 45455
200 | 350 | 0.01 | 3.5 | 100000

## Slide 14: IR cameras. FLIR vs TELOPS
Integration time
Max Photons = Max Energy = Φ3-5μm(T).τ
Data FLIR: F/2.5
Temp range (degC) | Pbb: Corresponding BB emissive power (Planck's law) integrated between 3mu et 5mu | Tint: Recommended integration time | Ebb=Pbb*Tint: Energy emitted by the BB during the integration time | Maximum frame rate based on integration time
degC | W/m2/mu | ms | J/m2/mu | Hz
-20 to 50 | 0.78 to 15 | 1.1424 | 0.89 to 17.14 | 875
10 to 90 | 3 to 39 | 0.472 | 1.42 to 18.41 | 2119
35 to 150 | 7.7 to 148 | 0.1321 | 1.02 to 19.55 | 7570
80 to 200 | 30.3 to 350 | 0.0568 | 1.72 to 19.88 | 17606
150 to 350 | 148 to 2130 | 0.0094 | 1.39 to 20.02 | 106383
Data Telops: F/2.5 + fill factor 100pc
Temp range (degC) | Pbb: Corresponding BB emissive power (Planck's law) integrated between 3mu et 5mu | Tint: Recommended integration time | Ebb=Pbb*Tint: Energy emitted by the BB during the integration time | Maximum frame rate based on integration time
degC | W/m2/mu | ms | J/m2/mu | Hz
0 | 1.988 | 0.7089 | 1.4093 | 1411
50 | 12.6 | 0.2806 | 3.5356 | 3564
100 | 50 | 0.0886 | 4.4305 | 11285
150 | 148 | 0.0325 | 4.8086 | 30778
200 | 350 | 0.0148 | 5.1690 | 67712

## Slide 15: IR cameras. FLIR vs TELOPS
Integration time
Max Photons = Max Energy = Φ3-5μm(T).τ
FLIR
Telops

## Slide 16: IR cameras. FLIR vs TELOPS
Noise: NEdT
NEdT = StdDev(I)*ΔT/ ΔI
FLIR: 18mK
Telops: 18mK

## Slide 17: IR cameras
Lens collection
  Emission from source through lens
    Flux through lens: dΦ=Eemis(T).cos(θ).Ω.dA
    Solid angle: Ω=(π/4).(d/z)2.cos(α)3
  Collection on sensor:
    dΦ=Ecoll(T).dP => Ecoll(T)=Eemis(T).cos(θ).Ω.dA/dP
    Only depends on lens aperture and of angle α

## Slide 18: Transmission sapphire
http://www.google.com/url?sa=t&rct=j&q=&esrc=s&frm=1&source=web&cd=8&cad=rja&uact=8&ved=0CFYQFjAH&url=http%3A%2F%2Fwww.springer.com%2Fcda%2Fcontent%2Fdocument%2Fcda_downloaddocument%2F9780387856940-c1.pdf%3FSGWID%3D0-0-45-719708-p173851708&ei=wWZFU8uAOrTUsAT404DABA&usg=AFQjCNGmYizK7Mr9JX6iAJXR5zeYsQ3ogQ&bvm=bv.64507335,d.dmQ

## Slide 19: Detection of vaporized fuel
Case of study: IR camera looking at the spray from the side
Collected IR
Along the gray arrow, the intensity I evolves as:
dIλ/dr = κλIbλ- κλI λ(r)
Where κλ = αλ.c(r),
αλ being the absorption coefficient and c the concentration of the fuel
r
z
y

## Slide 20: Detection of vaporized fuel
Look a cross-section of the spray at distance z
Collected IR
r
z
y
Iλ(r+dr) = Iλ (r)+ αλ.c(r).[Ibλ- I λ(r)]
For n-heptane, at 3.4µm, we have abosrbance:
A=log(I/I0) ≈ 1.9, for 30mmHg n-Heptane and a path length of 0.05m, at 20°C.
This gives αλ=-ln(10αλ)/(L.c)≈70 (mol.m-3)-1.m-1
Emission collected by the camera
=> Apparently, no decrease of the signal in the spray tip region (higher temperature), which should make the detection of the borders of the spray quite easy.

## Slide 21: Detection of vaporized fuel
Abs. Coef.: 0.01cm-1 @3.4µm
Thickness: 2cm
Self-emission: 42W/m2
Transmission: 98%
Wall
Sapphire window
Self-emission from the spray
Total absorption of the spray
BG noise from wall
Relevant signal
S/N

## Slide 22: Detection of vaporized fuel
Effect of absorption coefficient α
α =70 (mol.m-3)-1.m-1
α =1 (mol.m-3)-1.m-1
α =1000 (mol.m-3)-1.m-1
Self-emission of the spray
Total absorption of the spray
Cross-section emission of the spray

## Slide 23: Emission from a sample of fuel
Fuel at cst Φ
T: adiabtic mixing
P=60b
L=20mm
Normalized emission (a.u.)

## Slide 24: Precision of the measurements
NETD:
  Camera looks at a scene at constant temperature.
  Pi(t): value of pixel #i at instant t
  μi: temporal average of Pi(t)
  σi: standard deviation of Pi(t)
  NETD=average value of σi for all the pixels of the chip, converted into temperature (NETD=NETDcounts*ΔT/Δcounts).
σi
NEDT
σNEDT
For Telops FAST-IR 1500, NETD ≈23mK, and σNEDT ≈5-6mK.
For FLIR SC6800, NETD<20mK.

## Slide 25: Precision of the measurements
Accuracy:
  Camera looks at a scene at constant temperature T0.
  Pi(t): value of pixel #i at instant t
  μi: temporal average of Pi(t)
  For different sensors, T0 – μi follows a gaussian function. Its standard deviation is the accuracy.
μi
T0
Accuracy
For Telops FAST-IR 1500, accuracy is +/-1oC.
For FLIR SC6800, accuracy is +/-2oC.

## Slide 26: Impact of measurement errors on heat flux results
Surface temperature T can be decomposed in Fourier series:
Then, the transient part of the heat flux is given by:
Tw(t)
Tw(t)+noise
q